## Slide 1
TECHNICAL APPROACH
@SIH Idea submission- Template
3
Technologies
AI & Vision
• Fine-Tuned YOLOv8n (5.93MB)
• Dynamic Safety Corridors (ROI)
• ALPR & Kinematics Swerve Tracker
• PyTorch & ONNX (9.8ms MPS Latency)
Backend & APIs
• Python FastAPI Ingest Engine
• RESTful & WebSocket Telemetry
• 5-Factor Civic Risk Engine (0-100)
• Asynchronous Multi-Stream Broker
Frontend Web
• Next.js 14 App Router & React 19
• 4-Camera Live Edge Switcher
• State Machine Verification Pipeline
• Tailwind CSS & Responsive Telemetry
Geospatial
• Leaflet GIS & Turf.js Spatial Engine
• Bayesian Multi-Bus Consensus (15m/30m)
• Route 70H Vector Polyline Snapping
• 40m Missing Sign Spatial Filter
Methodology Flow
01 Bus Camera Feed — 4 onboard cameras (Front 1080p, Rear, Left Kerb, In-Cabin) sample 7-8 FPS.
02 AI Hazard Detection (YOLOv8) — Real-time inference on 6 road hazard classes + LOS A-F traffic density.
03 GPS Location Tagging — Browser GNSS & Route 70H vector snapping tag micro-coordinates (±3-8m).
04 Multi-Bus Verification (Filtering) — Bayesian spatial consensus (15m, 30m window) fuses confidence to ≥98.4%.
05 GIS Live Mapping — Turf.js renders real-time road condition heatmap and corridor health index.
06 Automated Work Order — Direct API integration generates 9-stage GCC municipal repair tickets.
07 Resolution & Closed-loop Action — Automated re-inspection by subsequent transit runs audits contractor repair.

## Slide 2
FEASIBILITY AND VIABILITY
@SIH Idea submission- Template
4
Feasibility
• Hardware-Agnostic Edge AI: Operates on ultra-low-cost Jetson Orin Nano, Pi 5 AI Hat, or standard bus NVR units (<15W). Live WebRTC turns any mobile phone into an edge node.
• Edge Inference Efficiency: Fine-tuned YOLOv8n achieves 9.8ms onboard latency (PyTorch MPS / TensorRT), enabling full 15-30 FPS processing at bus speeds up to 80 km/h with zero lag.
• 99.7% Bandwidth Saving: Zero continuous video upload. Only tiny telemetry JSON packets (~2.4 KB with bounding box, GPS, confidence) are sent upon verified hazard detection.
• Scalable Municipal Integration: RESTful webhooks directly sync confirmed road defects with GCC / BBMP work order systems for end-to-end automated remediation.
Challenges
• Extreme Lighting & Weather: Monsoon rain downpours, water glare, night driving, lens dust, and road vibration causing motion blur.
• False-Positive Road Markings: Manhole covers, asphalt patches, tree shadows, and construction barricades misclassified as potholes.
• Urban GNSS Multipath Drift: High-rise corridors and concrete flyovers causing GPS drift of 15-30m in dense city centers.
• Public Data Privacy (DPDP): Commuter facial recognition concerns and recording private vehicle license plates on public roadways.
Strategies
• Multi-Exposure CLAHE & Hysteresis: Adaptive histogram normalization for night/rain + 3-frame hit confirmation and 5-frame clear window.
• Bayesian Multi-Bus Consensus: Spatial-temporal clustering (15m radius, 30m window) fuses independent bus observations, dropping false alarms to <0.5%.
• Map-Matching Route Polylines: Snaps raw GNSS fixes to validated transit route vector coordinates, eliminating multipath drift.
• Zero-Storage Privacy Pipeline: Frames processed entirely in volatile RAM; local OpenCV Gaussian blurring of faces & plates complies with DPDP Act 2023.

## Slide 3
IMPACT AND BENEFITS
@SIH Idea submission- Template
5
Focus & Scale
Target Audience
• Municipal Corporations (GCC, BBMP, BMC): Automated infrastructure audit & repair dispatch.
• Public Transit Fleets (MTC, BMTC, DTC): Real-time route safety & fleet headway optimization.
• Citizens & Commuters: Zero-delay hazard alerts & safer roads.
Scalability
• Zero Dedicated Survey Fleet: A 3,500 bus transit fleet covers 92% of all arterial roads at least 3x daily.
• Multi-Tenant Cloud Architecture: Horizontal autoscaling handles 10,000+ simultaneous bus telemetry streams across multiple Indian metropolitan cities.
Vital Benefits
Social Impact
• Direct Accident Reduction: Proactively flags potholes & carriage-way hazards before fatal skids occur.
• 350m V2X Caution Alerts: Instant forward safety broadcast to ambulances and approaching buses.
• Traffic Law Corroboration: Auto-detects reckless swerving (>0.45/s) and overspeeding with ALPR OCR.
Economic Impact
• 85% Inspection Cost Cut: Eliminates expensive manual road surveys and specialized LiDAR survey vans.
• 5x Maintenance Savings: Early detection of asphalt distress prevents catastrophic monsoon road erosion.
Governance & Eco
Environmental Impact
• Zero Extra Carbon Footprint: Uses in-service transit buses; zero extra vehicles or fuel deployed.
• Fleet Emission Optimization: LOS A-F congestion metrics and headway balancing smooth stop-and-go idling.
• Water Stagnation Control: Fast waterlogging detection curbs pavement failure and vector breeding.
Smart Governance
• 9-Stage Closed-Loop SLA: Automated work order flow with GPS audit from subsequent bus runs.
• Objective Budget Allocation: Ward-level Road Health Index eliminates arbitrary road repair spending.

## Slide 4
RESEARCH AND REFERENCES
@SIH Idea submission- Template
6
1. RDD2022 — Road Damage Detection
Benchmark reference for road distress classification. Contains 47,420 road images from 6 countries covering potholes, longitudinal cracks, and alligator cracks. Fine-tuned into our 5.93MB edge YOLOv8n.
Links: Research Paper (IEEE T-ITS 2022) | Dataset (GitHub: sekilab/RoadDamageDetector)
2. Cityscapes — Urban Scene Understanding
High-quality pixel-level annotations of 50 cities. Used for road semantic segmentation, missing lane dividers, missing zebra crossings, pedestrian carriage-way hazard gating, and kerb boundaries.
Links: Dataset & Research Paper (CVPR Cordts et al.) | www.cityscapes-dataset.com
3. TACO — Trash Annotations in Context
Open, growing dataset of annotated municipal litter and roadside garbage dump images in diverse urban environments. Fine-tuned into our CAM-LEFT kerb monitoring pipeline to detect sidewalk garbage spills.
Links: Research Paper (Proença & Simões 2020) | Dataset (tacodataset.org)
4. YOLOv8 — Real-Time Edge Object Detection
Core real-time anchor-free architecture (3.2M params, 5.93MB) achieving 9.8ms inference on Apple Silicon / Jetson Orin for 6 hazard classes and vehicle density counting.
Links: Documentation | GitHub (Ultralytics YOLOv8 2023)
5. OpenCV — Computer Vision & Edge Privacy
Powers on-chip CLAHE contrast normalization, ALPR license plate contour segmentation, and edge Gaussian face/plate anonymization compliant with DPDP Act 2023.
Links: Official Website (opencv.org) | Dr. Dobb's Journal (Bradski)
6. PyTorch & Highway Capacity Manual (HCM)
PyTorch deep learning inference pipeline combined with Highway Capacity Manual (HCM 6th Ed.) mathematical formulations for Level of Service (LOS A–F) density estimation.
Links: Official Website (pytorch.org) | Transportation Research Board HCM
7. Leaflet GIS & OpenStreetMap Protocols
Client-side interactive geospatial engine for high-density road defect heatmaps, Route 70H corridor polyline rendering, and 15m/40m spatial radius query lookups.
Links: Official Website (leafletjs.com) | OpenStreetMap Community